### IMU + Vibrations and attitude
Be sure to always mind following constraints:
- mechanical damping until all vibrations are at least withing measurement range at all frequencies : (careful in very small vehicles this vibration might be of higher frequency than the sensor can measure: e.g. 1kHz 20g vibration on aspirin will be seen as measurements of only 6 to 8g while gravity is becomes 0.5g instead of 1g, so not always obvious)
- 机械阻尼,直到所有的振动频率至少在测量范围
  (要小心在非常小的飞行器上的振动频率可能比传感器可以测量的频率更高:如1 khz 20 g振动对阿司匹林的将被视为测量只有6到8 g而引力是变成了0.5 g而不是1 g,所以并不总是显而易见的)
- accelerometer should be filtering BEFORE AHRS computations but with minimal lag (a sudden 45 deg roll should not be counter-compensated for 0.5 seconds just because the accelerometer is slow). With mechanical damping at least gyro and accelero feel the same motion.
- 加速度计应在AHRS计算并且以最小的延迟滤波
  （突然45度翻滚应该没在0.5秒没有被补偿计算仅仅因为加速度计是缓慢的）
  至少机械阻尼陀螺和加速度计感到同样的运动。
- gyro filtering should be AFTER INTEGRTION in ahrs since simple filtering (e.g. xf = (xm-xf)/K ) can distort the integral
- 陀螺仪滤波应该在积分之后在导航中，以来明显简单的过滤（e.g. xf = (xm-xf)/K）会扭曲的积分
- in AHRS with V x omega as compensation for centripetal force: omega is often filled with gyro measurements while in theory it should be the turn rate or looping rate. Short period dynamics of the plane should be filtered out first: e.g. at 20m/s during a 10deg/sec turn (=0.35g) a gust easily makes a 300deg/sec short period oscillation (=10.5g which is not present and not measured either and very quickly screws attitude)
- 在导航中以Vx ω作为向心力的补偿：ω是经常充满了陀螺测量在理论上应该是转率或循环率。短时间内飞机的动力应该是先过滤掉：如在20 m / s 10度/秒转(= 0.35 g)一阵轻松300度/秒短周期振荡(= 10.5 g,不存在,不是衡量,和很快的螺旋姿态)
#### Complementary AHRS
In the AHRS type int_cmpl_quat there is a heuristic that scales down the usage of the accelerometer if deviations from 1g are measured. This can potentially improve the state estimate as dynamic accelerations are not compensated for in the filter. However, if large deviations from 1g are continuously measured due to vibrations, the accelerometer is not used most of the time. This will cause the attitude estimate to drift. In this case, it is better not to use the heuristic and define AHRS_GRAVITY_HEURISTIC_FACTOR to 0 in the airframe file.
在导航类型int_cmpl_quat启发式尺度下的使用加速度计测量如果偏离1 g.这可以提高状态估计的动态加速度不补偿滤波器.
然而,如果大偏离1 g不断测量由于振动,不使用加速度计的大部分时间.这将导致态度估计漂移.在这种情况下,最好不要使用启发式和定义AHRS_GRAVITY_HEURISTIC_FACTOR 0在机身文件中。
### Measuring Vibration
In the Telemetry tab of the Settings tool, enable the collection of scaled sensor messages (scaled_sensors). Remember to commit the selection by pressing the green checkmark button.
Once the data is logged, the report_imu_scaled tool is used to quickly analyze and generate metrics related to the captured flight data.
在遥测选项卡的设置工具,实现了传感器信息的收集(scaled_sensors)。记得提交选择按下绿色的对号按钮.一旦数据记录,report_imu_scaled工具用于快速分析和生成指标相关飞行数据捕获。

#### Accelerometer (Vibration)
ACCEL : Time Range(100.006 : 220.982)
        ax ay az
Min [ -2.413 -2.507 -24.158] m/s2
Max [ 2.170 2.066 7.477] m/s2
Mean [ -0.019 -0.580 -9.549] m/s2
StDev [ 0.731 0.758 5.936] m/s2

#### Gyroscope
GYRO : Time Range(100.342 : 220.998)
        gp gq gr
Min [-50.358 -47.924 -38.048] deg/s
Max [ 51.574 47.000 25.668] deg/s
Mean （平均） [ 0.661 0.019 -0.849] deg/s
StDev(标准差) [ 17.431 15.366 5.136] deg/s

#### Magnetometer (EMI)
MAG : Time Range(100.022 : 220.934)
        mx my mz
Min [ -0.534 -0.594 0.953] unit
Max [ 0.089 0.000 1.079] unit
Mean [ -0.201 -0.405 1.019] unit
StDev [ 0.163 0.083 0.019] unit